SAFE WORK METHOD STATEMENT – Part 1

| Company Details |
| --- |
| Company Name: CJR Concrete Pumping Pty Ltd | ABN: 50 126 931 413 |
| Contact Name, Position and Phone number: Chris Reitano, Director, 0412 055 024 |
| Address: PO Box 1226, Maroubra NSW 2035 |
| Project details |
| Project: | Area: |
| Job Address: |
| Job Description: |
| Activity: Concrete Line Pumping |
| Relevant workers must be consulted in the development, approval and communication of this SWMS | SWMS Approved by: | Page 1 of 11 |
| Name: (Include names of workers who were consulted in relation to this SWMS) | Signature: | Job Title: | Date: | Name: |
|  |  |  |  | Signature: |
|  |  |  |  | Date: |
| Personnel responsible for monitoring and managing activity: | Overall Risk Rating After Controls | 4 Acute | 3 High |
|  |  | 2 Moderate | 1 Low |
| ALL PERSONS INVOLVED IN TASK MUST HAVE THIS SWMS COMMUNICATED TO THEM PRIOR TO WORK COMMENCING Regular inspections and observations will be conducted by Chris Reitano to ensure SWMS is being complied with. Daily Tool Box Talks will be undertaken to identify, control and communicate additional site hazards. Work must cease immediately if incident or near miss occurs. SWMS must be amended in consultation with relevant persons. Amendments must be approved by Chris Reitano and communicated to all affected workers before work resumes. SWMS must be made available for inspection or review as required by WHS legislation. Record of SWMS must be kept as required by WHS legislation (until job is complete or for 2 years if involved in a notifiable incident). |

Personal Protective Equipment

Foot Protection Hearing Protection High Visibility Head Protection Eye Protection Hand Protection Protective Clothing Day Operations – Normal Requirements: Safety footwear, hearing protection, high visibility shirt or vest, hard hat and sun protection if required eye/face protection (goggles), hand protection (gloves), waterproof clothing. Ensure all PPE meets relevant Australian Standards. Inspect, and replace PPE as needed. Provide UV sun protection where required, (broad brimmed hat, UV rated clothing, SPF 30+ sunscreen, tinted safety glasses with adequate UV protection).

Safety Notes

This SWMS covers the delivery of concrete via line pumping. Main hazards include: Contact with fluid under pressure Entanglement Electric shock/electrocution

| Task Breakdown | Possible Safety or Environmental Hazards | RB | Control Measures to Reduce risk | RA | Responsible Officer |
| --- | --- | --- | --- | --- | --- |
| NOTE: RB = Risk Rating before controls implemented - RA = Risk Rating after controls are implemented. |
| Planning | Personal Injury: Slips, trips, falls Contact with high pressure fluids Hit by moving vehicle Electric shock Legislation breach: Failure to obtain permits Environmental Damage: - Pollution from concrete residue. | 4A | Assess site. Ensure: Ground is firm and stable Safe access/egress (free of tripping hazards) Room for access equipment (cranes, hoists etc) No work within 3m of overhead electric lines Concrete pump able to be positioned safely (allows for visual contact between pump operator and pour area, not positioned over or adjacent to previously disturbed or back-filled land, excavations, trenches, pits etc and on level ground) Defined pump washout area that complies with EPA and local laws Method to collect concrete residue to prevent wash-off entering sensitive areas (such as storm water drains) Compressed air and water lines are set-up to prevent damage and meet relevant Australian Standards Lines can be placed in a safe manner without risk of movement or damage or run over by plant. Workers are not exposed to site hazards (such as building work overhead, unsafe electrical installations, close proximity to moving plant/vehicles etc). Underground assets are not impacted (dial before you dig) Sufficient lighting Sufficient warning signs and exclusion zones Permit etc are obtained as required. Ensure: Sufficient time for job, number of workers and communication systems | 2M |  |
| Planning - continued | Personal Injury: Slips, trips, falls Contact with high pressure fluids Hit by moving vehicle Electric shock Legislation breach: Failure to obtain permits Environmental Damage: - Pollution from concrete residue. | 4A | Obtain advice from competent persons (such as an engineer). Include: Type of materials (pipes, clamps, anchor brackets) Pressure requirements/limitations Instructions for layout of pipes and correct sequence Type, number and placement of anchor points tie-downs, legs, bolts etc) Determine access areas for concrete delivery and hopper. Ensure: Ground is firm and stable with sufficient room. Hopper positioned at correct height to allow for gravity flow into hopper (if ramps used, ensure non-slip, correctly spaced so that truck remains stable). Traffic management (for reversing vehicles, for roadway obstruction and other factors as required) Number of trucks kept to minimum – ensure adequate communication. Use Spotter if required. Clear of overhead electric lines. Use Spotter if required. Seek council approvals as required. Ensure all equipment is in a safe condition. Conduct inspections before use. Ensure: Pumps have guards in place, in good working order and regularly maintained Hopper has guards/grill is place to prevent access to agitators and other moving parts Emergency stop buttons in place for concrete delivery systems Electrical equipment is rated for environment, RCDs are provided and cables/leads are in safe condition PPE is clean, serviced and appropriate for task. Rubber hoses are not damaged or cracked. Develop task specific SWMS. | 2M |  |
| Preparation | Personal Injury: Slips, trips, falls Contact with high pressure fluids Hit by moving vehicle Electric shock | 3H | Ensure permanently fitted legible identification on pieces. When laying a pipeline, ensure: All pieces are inspected before use Unnecessary bends are avoided Horizontal pipelines are adequately supported Flexible hoses are not at risk of being run over/damaged Each section of pipe in a vertical pipeline is supported to avoid extra load on the pipe clamp The 90 degree bend at the base altering the direction of the concrete line from horizontal to vertical is equipped with a firmly sitting leg on the ground sufficient to stop any movement in the vertical line which may snap off the first clamp Vertical lines are secured to the building Cranes or hoist towers, scaffolding or formwork are not used to secure the line (may not be capable of taking the impact load when pumping concrete through line) Metal pipes and pipeline components are identified and checked in accordance with AS2550.15. For Quick release pipe clamps, ensure: Able to sustain the maximum concrete pressure applied to line Locking pins are present and secured (do not use clamps without locking pins) Regularly inspected for wear or fatigue Damaged clamps are not used Clamps are locked as per manufacturers instructions (not by hammering the lever) Ensure piping in kept in parallel to ground when setting up near overhead electric lines. Use spotter as required. | 2M |  |
| Concrete Delivery | Personal Injury: Hit by moving vehicle | 3H | Delivery vehicle to park in designated area and follow traffic management for site. Ensure: Trucks only reverse if visual contact can be made with Spotter (or nominated person) No persons to stand between reversing truck and hopper Concrete chute only be moved when truck is stationary. Communicate with driver as required. | 2M |  |
| Operation | Personal Injury: Slips, trips, falls Contact with high pressure fluids Hit by moving vehicle | 3H | Operate pump as per manufacturer’s specifications. Do not leave pump unattended. Ensure pump flow rates match discharge rates of delivery trucks. Follow site specific SWMS and work directions. Check pipelines continuously for unusual movement, shaking or pressure release. Where excessive pipe movement occurs due to the surging action of the pump: Use extra anchorage to restrict the line movement, especially at bends and elbows, or Install a short wire-braided high pressure rubber hose between the concrete pump and pipelines in accordance the manufacturer’s recommendations. | 2M |  |
| Line cleaning | Personal Injury: Contact with fluid under pressure | 3H | Follow manufactures instructions. Ensure: Unessential persons removed from area, especially discharge end All persons to wear required PPE High pressure water (not air) is used Air-relief valves are present and working Relieve pressure before dismantling Don’t leave unattended until internal pressure is gone Remove rubber hose at end and secure all parts to prevent accidental movement Suitable catchment device/receptacle (such as concrete truck bowl) is used | 2M |  |
| Pump cleaning | Personal Injury: - Entanglement | 3H | Ensure guards in place. Ensure hopper is isolated from power, any accumulated hydraulic or air pressure is released, and the hopper cannot be accidentally energized before persons enter or insert any body parts for cleaning, repairs, or removing blockages. Clean as per manufacturers’ instructions. | 2M |  |
| Maintenance | Personal Injury: Slips, trips, falls Contact with high pressure fluids Hit by moving vehicle Electric shock Environmental Damage: - Pollution from concrete residue. | 4A | Ensure all equipment undergoes regular maintenance as required by manufacturer. Regular pipe testing must be undertaken as per AS2550.15. Ensure pipe log books are maintained detailing wall thickness and pressure details (as per AS 1418.15). | 2M |  |

References:

Model Work Health and Safety Act 2011 and Model Work Health and Safety Regulations 2011

QLD DEIR (2005) Code of Practice for Concrete Pumping

AS 2550.15 (1994) Cranes – Safe Use – Concrete Placing Equipment

AS 1418.15 (1994) Cranes (including hoists and winches) – Concrete Placing Equipment

WorkCover NSW (1994) Concrete Pumping

WorkSafe Victoria (2004) Concrete Pumping Industry Standard

NATIONAL STANDARD FOR PLANT [NWHSC:1010]

SAFE WORK METHOD STATEMENT – Part 2

| Formal Training, Licenses required for workers undertaking this task: | Duties of workers undertaking this task: | Training in the following safe work procedures/ SWMS / training modules is required: (All workers to be trained in relevant procedures.) |
| --- | --- | --- |
| On Job training – no formal qualification | Operator linesman | Site-specific inductions Training in this SWMS Nature of hazards / risks Emergency procedures |
| Details of Supervisory Arrangements for workers undertaking this task: | Details of regulatory permits/licenses, Engineering Details/Certificates/WorkCover Approvals: | Relevant Legislation, Codes of Practice: |
| Competent supervisors for job Direct on-site supervision Remote site – communication systems/ schedule Audits Spot Checks, etc Reporting systems | Local council permits Building Approvals EPA approvals/permits PPE to comply with relevant Australian Standards | Model Work Health and Safety Act 2011 and Model Work Health and Safety Regulations 2011 QLD DEIR (2005) Code of Practice for Concrete Pumping AS 2550.15 (1994) Cranes – Safe Use – Concrete Placing Equipment AS 1418.15 (1994) Cranes (including hoists and winches) – Concrete Placing Equipment WorkCover NSW (1994) Concrete Pumping WorkSafe Victoria (2004) Concrete Pumping Industry Standard NATIONAL STANDARD FOR PLANT [NWHSC:1010] |
| Plant/Tools/Equipment: (List plant and equipment to be used on the job.) | Maintenance Details for plant / equipment used on job (Include cranes, forklifts, electrical equipment etc.) |
| N/A | N/A |

Part 3- SIGN OFF

This SWMS has been developed in consultation and cooperation with workers and relevant Persons Conducting Business or Undertaking (PCBU). I have read the above SWMS and I understand its contents. I confirm that I have the skills and training, including relevant certification to conduct the task as described. I agree to comply with safety requirements within this SWMS including safe work instructions and Personal Protective Equipment described.

| Name | Qualifications | Signature | Date | Time | PCBU |
| --- | --- | --- | --- | --- | --- |

| Review No. | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Name and initials |  |  |  |  |  |  |  |  |  |
| Date |  |  |  |  |  |  |  |  |  |

Part 4- RISK ASSESSMENT

Risk Management Code of Practice 2007, AS/NZS 31000 -2009 Risk Management Principles and guidelines

Step 1	Determine Likelihood – What is the possibility that the effect will occur? 			Step 2	Determine Consequence - What will be the expected effect?

|  | Criteria | Description |
| --- | --- | --- |
| Almost certain | Expected in most circumstances. | Effect is a common result |
| Likely | Will probably occur in most circumstances. | Effect is known to have occurred at this site or it has happened |
| Possible | Might occur at some time | Effect could occur at the site or I’ve heard of it happening |
| Unlikely | Could occur at some time | Effect is not likely to occur at the site or I have not heard of it happening |
| Rare | May occur only in exceptional circumstances | Effect is practically impossible. |

| Level of Effect | Example of each level |
| --- | --- |
| Insignificant/Acceptable | No effect – or so minor that effect is acceptable |
| Minor | First aid treatment only; spillage contained at site. |
| Moderate | Medical treatment; spillage contained but with outside help. |
| Major | Extensive injuries; loss of production |
| Catastrophic | Death; toxic release of chemicals |

Step 3 Determine the risk score						  		Step 4 Record risk score on worksheet (Note – Risk scores have no absolute value and should only be used for comparison and to engender discussion.)

|  | CONSEQUENCE |
| --- | --- |
| LIKELIHOOD | Insignificant | Minor | Moderate | Major | Catastrophic |
| Almost certain | 3 High | 3 High | 4 Acute | 4 Acute | 4 Acute |
| Likely | 2 Medium | 3 High | 3 High | 4 Acute | 4 Acute |
| Possible | 1 Low | 2 Medium | 3 High | 4 Acute | 4 Acute |
| Unlikely | 1 Low | 1 Low | 2 Medium | 3 High | 4 Acute |
| Rare | 1 Low | 1 Low | 2 Medium | 3 High | 3 High |

| Score | Action |
| --- | --- |
| 4 A: Acute | ACT NOW – Urgent - do something about the risks immediately. Requires immediate attention. |
| 3 H: High | Highest management decision is required urgently. |
| 2 M: Moderate | Follow management instructions. |
| 1 L: Low | OK for now. Record and review regularly, and if any equipment/ people/ materials/ work processes or procedures change. |